## Slide 1
Caracterization study of the human skin
MASTER’S DEGREE FINAL PROJECT – MASTER OF ENGINEERING
Wassim Ourkiya, Vincent Maison, Kamel Loukkas, Sohan Lindor, Oumaima Krimech and Corentin Chan
Supervisor : Pr. Stéphane Holé (ESPCI), in charge of Sensor, Measurement and Instrumentation (CIMES) specialization
(2) Absorption coefficients of different chromophores
(1) Schematic diagram of optical pathways in human skin
Skin – Light Interaction
Identify skin chromophores with spectroscopy
Analysing scattering diagram, for each angle
Instrumentation
Light isolated environnement
Skin sample is lighten up with a LED by converging light through lenses
Reflected light captured by the sensor (photodiode)
Stepper motor providing rotational movement, several angles during the measurement
Signal sampling by a micro controller
Experimentation results
(3) Descriptive diagram and schematic of the system
Integration of the absorption spectrum of the skin :
∫𝑆𝐸∗𝑆𝑆∗𝑆𝑅 𝑑𝜆 ; 𝑆𝐸, 𝑆𝑆, and 𝑆𝑅 are
respectively the spectrum of
emission, diffusion and receiver
(4) Spectral response of the emitting (a, 5050 LED) and receiving (b, OSD 35-7X CQ) components
Acquisition
(5) Skin sample area used for each subject, as input of the acquisition system
(4) Block-diagram of the recognition system
Discretization of the rotational movement
Conversion of photocurrent into data used in programming environnement
Measuring the absorption spectrum with a spectrophotometer
Vein segmentation through a camera mounted on the motor
Multimodal recognition, biometric application
7 healthy subjects in order to chromophores identification
4 subjects to test and compare dry and humid skin, via spectroscopy
Scattering diagram analysis for each angle
Extraction of error bars (input data for recognition tool)
Pattern recognition -> 100% accuracy
Perspectives
- R. R. Anderson and J. A. Parrish, “The Optics of Human Skin,” J. Invest. Dermatol., vol. 77, no. 1, pp. 13–19, Jul. 1981.
- K. S. Bersha, “Spectral imaging and analysis of human skin,” University of Eastern Finland, 2010.
- L. Hode, Penetration of light into living tissue. 2012.
- J. K. Wagner, C. Jovel, H. L. Norton, E. J. Parra, and M. D. Shriver, “Comparing quantitative measures of erythema, pigmentation and skin response using reflectometry,” Pigment Cell Res., vol. 15, no. 5, pp. 379–384, Oct. 2002.
- J. J. Riesz, The spectroscopic properties of melanin. University of Queensland, 2007.
- T. Vo-Dinh, Biomedical Photonics Handbook. CRC Press, 2003.
(5) Spectrum of skin samples acquired from right back of hand of each seven subjects
(7) Polar scattering diagram of subjects
(6) Recognition rate for the two modalities of the recognition task.
(5) Fujitsu PalmSecure Palm Vein, biometric authentication device
(5) Sony’s Smart Skin Evaluation Program, analyzing various elements of the skin
Improved system with a monochromator in order to have a great dimensionality as input of recognition data as well as higher accuracy for wide range of different data
Maximized signal-to-noise ratio by minimizing standard deviation.
Coupled system with a camera for a better clustering
Adaptation for different application in different fields of study such as medical, cosmetology, computer graphics as well as biometrics.
© Fujistu
© Sony